PL-84

SUBJECT: RVSM OPERATIONS

------------------------------ MMEL GLOBAL CHANGE-----------------------------

PL-84 is designated as GC-33

This GC is an approved addendum to all existing MMEL

documents.  The operator may seek use of the specific relief

contained in the policy letter by revising the Minimum

Equipment List (MEL).  In doing so, the sample proviso stating

the relief in the policy letter must be copied verbatim in the

operator's MEL.  Approval of the revised MEL is gained

utilizing established procedure, through the assigned

Principal Operations Inspector (POI).

=============================================================================

INFORMATION:   Policy Regarding Aircraft System Requirements

for Reduced Vertical Separation Minimum (RVSM)

Operations in the MMEL

July 18, 1996

Manager, Air Transportation Division,  AFS-200

All Regional Flight Standards Division Managers

All AEG Managers

Following discussion with members of the aircraft evaluation

groups, operations and maintenance personnel at

headquarters, and with industry, the Flight Operations

Policy Board (FOPB) has established the following policy.

DISCUSSION

Since the 1950's, 1,000 foot vertical separation has been

applied up to Flight Level (FL) 290 and 2,000 foot vertical

separation has been applied above FL 290.  The RVSM program

enables 1,000 foot vertical separation to be applied between

FL 290 and FL 410 based on FAA approval of operator aircraft

altitude-keeping capability, continuing airworthiness and

operations programs.  The following systems  are required to

be installed on aircraft to be approved to conduct RVSM

operations:  two (2) independent altitude measurement

systems (as defined in FAA Interim Guidance 91-RVSM,

paragraph 8a), one (1) secondary surveillance radar (SSR)

reporting transponder, one (1) altitude alerting system, and

one (1) automatic altitude control system.  In addition,

there is an operational requirement for certain systems to

be operating at entry into airspace where RVSM is applied.

They are:  two (2) independent altitude measurement systems,

one (1) altitude alert system, and one automatic altitude

control system.

POLICY

PL-84

The FOPB has determined that the MMEL's for aircraft

approved to operate in RVSM airspace should reflect dispatch

requirements for certain aircraft systems that provide

altitude-keeping capability.  Accordingly, the following

requirements must be addressed:

TWO (2)  independent altitude measurement systems comprised

of the following elements:

-Cross coupled static source system provided with ice

protection if located in areas subject to ice accretion

-Equipment for measuring static pressure sensed by the

static source, converting it to pressure altitude, and

displaying pressure altitude to the flightcrew

-Equipment for providing a digitally coded signal

corresponding to the displayed pressure altitude, for

automatic altitude reporting purposes

-Static source error correction (SSEC), if required to

meet RVSM altimetry system error requirements

-Equipment to provide reference signals for automatic

altitude control and alerting systems

One (1) SSR altitude reporting transponder

One (1) altitude alert system

One (1) automatic altitude control system capable of

automatically controlling the aircraft to a referenced

pressure altitude

Above guidance and generic equipment requirements reflect

the operational environment as it currently exists, and are

applicable to all aircraft dispatching into airspace where

RVSM is applied.  FOEB chairmen may need to assess specific

aircraft and systems independently where unique design

features and/or service history identify the need to address

"other" unspecified equipment requirements, e.g.,

operational limitations on the B-747 classic that may

mandate the use of auto-throttles to preclude unacceptable

mach excursions which can induce altimetry system errors.

EXAMPLE:

Altitude Alerting   A    -    0    (0)Except where enroute

operations require

System                                its use, may be

inoperative provided:

a) Autopilot with altitude

PL-84

hold is operative, and

b) Repairs are made within

three flight days.

Please review all MMELs for which you are responsible and

apply this policy to affected MMELs through the normal FOEB

process after giving operators as much notice as possible.

David R. Harrington

______________________________________________________________________